Self-priming Peripheral Pump XKSm 126

XKSm

Pump 
Self-priming peripheral pump

Liquid pumped temperature up to 60℃ 
Clean water, non-aggressive liquid with air

Specifications

| Model | Power | Inlet/Outlet | Max. Flow (L/min) | Max. Head (m) | Max. Suct (m) |
| --- | --- | --- | --- | --- | --- |
|  | (kW) | (HP) |  |  |  |  |
| XKSm126 | 0.125 | 0.17 | 1″×1″ | 40 | 32 | 8 |

Hydraulic Performance Curve

Motor 
Single phase/Three-phase, 50Hz/60Hz

Insulation class: 130
Protection class: IP44
Ambient temperature up to 40℃
With thermal overload protection

Parts Information of Self-priming Peripheral Pump

|  | Part | Material | Remark |
| --- | --- | --- | --- |
| 1 | Non-return valve | NBR |  |
| 2 | Pump cover | Brass |  |
| 3 | Impeller | Brass |  |
| 4 | Mechanical seal | Silicon carbide/Graphite |  |
| 5 | Pump body | Cast iron | Electrophoretic treatment, ABS |
| 6 | Front cover | Cast iron |  |
| 7 | Bearing | High quality |  |
| 8 | Rotor | Cold-rolled sheet | Welded stainless steel shaft |
| 9 | Capacitor | High quality |  |
| 10 | Stator | Aluminum casing | Cold-rolled sheet stator |
| 11 | End plate | Aluminum |  |
| 12 | Fan | Noryl |  |
| 13 | Fan cover | Noryl |  |

LEO is a renowned self-priming peripheral pump manufacturer and supplier in China. Apart from self-priming peripheral pumps, we also provide customers with other water pumps and garden machines, including centrifugal pumps, submersible pumps, garden shredders, lawn mowers, and more. As a result of their superior quality and reliability, they have received the GS, CE, UL, ETL, CB, EMC and EMF certification.  
Welcome to use LEO products! Thank you!